RX1 Communication Protocol

# Summary of Actuator Parameters:
- Torque Enable (0/1, address = 24)
- LED Status (0/1, address = 25)
- Goal Position (0-1023, address = 30(L), 31(H))
- Moving Speed (0-1023, address = 32(L), 33(H))
- Present Position (0-1023, address = 36(L),37(H))
- Present Speed (0-2047, address = 38(L),39(H))
- Present Load (0-2047, address = 40(L),41(H))
- Present Voltage (0-255, address = 42)
- Present Temperature (0-255, address = 43)
- Moving (0/1, address = 45)

# Base Message Structure
Byte	Value
0	Header of 0xFF
1	Header of 0xFF
2	Message ID
3	Number of data bytes (N)
4	Data byte
…
N+4	Checksum byte

# Message Details:

## Read Present Position for All Actuators
### Message:
Message ID = 0x20
Data = None
### Response:
Message ID = 0xA0
Data Size = 2 * number of actuators
Data:
- High byte for actuator 1
- Low byte for actuator 1
- High byte for actuator 2
- Low byte for actuator 2
- etc ...

## Read Present Speed for All Actuators
### Message:
Message ID = 0x21
Data = None
### Response:
Message ID = 0xA1
Data Size = 2 * number of actuators
Data:
- High byte for actuator 1
- Low byte for actuator 1
- High byte for actuator 2
- Low byte for actuator 2
- etc ...